## Slide 1: Pipeline Hazard Detection Simulator
CS 4200 – Computer Architecture
Jessica Webb

## Slide 2
Topic Overview
What Does It Simulate?
5 Stage RISC-V Pipeline: IF, ID, EX, MEM, WB
RAW (Read-After-Write) data hazards between instructions
Stall insertion
  Freezes IF/ID, inserts NOP bubble into EX
Cycle-by-cycle pipeline table output
Why Does It Matter?
Hazards cause the CPU to waste cycles, increasing CPI
Shows how dependent instructions impact real performance
Demonstrates the cost of forwarding not being interpreted
Compares hazard-free vs. hazard heavy programs

## Slide 3
Code Structure
Instruction Class
parse() method
Parse each line of RISC-V assembly
Identifies opcode, dest register (rd), and source registers
Supports R-type, I-type, load, store, branch
has_raw_hazard()
Hazard Detection
Checks ID-stage instruction against EX and MEM stages
Flags if a source register matches a dest still in flight
Skips x0 (never a real hazard)
run_pipeline
Simulation Engine
Advances instructions through 5 pipeline register each cycle
On hazard: freezes IF/ID, inserts NOP into EX
Tracks cycles, stalls, CPI, and full timeline

## Slide 4
Key Code: Hazard Detection
Check EX & MEM stages
Source vs. Destination
x0 is always 0
Any instruction still in the pipeline that hasn’t been written back can cause a hazard.
If a source register of the new instruction matches a destination not yet written back, that’s a raw hazard
Writing x0 has no effect, so hazards involving it are always ignored

## Slide 5
Results & Demo
HAZARD-FREE
BASIC HAZARDS
HEAVY HAZARDS
no_hazards.txt
basic_hazards.txt
heavy_hazards.txt
5
10
0
2.00
5
18
8
3.60
7
22
10
3.14
Instructions
Total Cycles
Stall Cycles
CPI
CPI
CPI
Stall Cycles
Stall Cycles
Total Cycles
Total Cycles
Instructions
Instructions

## Slide 6
Observations & Takeaways
01
02
03
04
Dependent chains cascade stalls
Same instruction count ≠ same performance
Forwarding would eliminate most stalls
Parsing edge cases matter
When every instruction on the previous one (heavy_hazards), each pair adds 2 stall cycles. Additionally, those stalls compound across the whole program.
no_hazards and basic_hazards both have 5 instructions, yet take 10 vs. 18 cycles. That is an 80% difference caused by data dependencies.
All detected hazards are 1-2 cycle gaps. Data forwarding (bypassing) would resolve them without stalling. This is a key real-world CPU optimization.
Handling commas, parentheses (offset addressing), and comments correctly was essential for the simulator to work on real RISC-V assembly syntax.